## Slide 1: Cache optimization using Anticipatory Prefetching
ANIRUDH.D.RATHI
KETAN.R.BHAVE
SHRINIWAS.S.AYYER

## Slide 2: Significance of Cache
Cache is an extremely fast memory used to store instructions that are repeatedly used by the CPU.
It accelerates the CPU instruction retrieval process and result in a more efficient system.
Without a cache, the CPU has to retrieve instruction directly from the RAM = time consuming, resulting in an inefficient system.

## Slide 3: Cache optimization
Performance of L1 cache is very critical.
Optimization means implementing techniques to affect certain metrics that improves the overall cache performance.
Our metric – Miss Rate

## Slide 4
Methods to reduce miss rate :
Larger block size
Larger cache size
Higher associativity
Cache optimization

## Slide 5: Project description
Objectives :
Evaluate the effect of caching parameters on cache performance.
Propose your own cache optimization.

## Slide 6: Project: Step 1
Evaluate the miss rate on a set of benchmark programs varying the Cache size and associativity.
    Cache sizes used – 8KB, 16KB, 32KB, 64KB
    Associativity – direct mapped, 2-way, 4-way
Select the best configuration

## Slide 7: Step 1: Results
Chart: 
| Direct Mapped | 2-way | 4- way | Direct Mapped | 2-way | 4- way | Direct Mapped | 2-way | 4- way | Direct Mapped | 2-way | 4- way | Direct Mapped | 2-way | 4- way | Direct Mapped | 2-way | 4- way | applu | apsi | cc1 | compress95 | fppp | hydro2d
8KB | 0.09471 | 0.0782 | 0.0699 | 0.0542 | 0.0327 | 0.0314 | 0.0765 | 0.0467 | 0.0303 | 0.0059 | 0.0054 | 0.0053 | 0.0917 | 0.0799 | 0.0721 | 0.0598 | 0.0546 | 0.0495
16KB | 0.0721 | 0.0646 | 0.0605 | 0.0302 | 0.023 | 0.0209 | 0.0437 | 0.0223 | 0.0121 | 0.0041 | 0.0016 | 0.0009 | 0.0783 | 0.0663 | 0.0618 | 0.0488 | 0.0439 | 0.0713
32KB | 0.067 | 0.058 | 0.0559 | 0.0188 | 0.0158 | 0.0127 | 0.0254 | 0.0103 | 0.0081 | 0.0011 | 0.0008 | 0.0003 | 0.0655 | 0.0598 | 0.0572 | 0.0434 | 0.0406 | 0.0596
64KB | 0.0595 | 0.05701 | 0.0552 | 0.0122 | 0.012 | 0.0115 | 0.0111 | 0.0077 | 0.0121 | 0.007 | 0.003 | 0.0003 | 0.0575 | 0.0564 | 0.0558 | 0.0406 | 0.0391 | 0.0596

## Slide 8: Step 1: Results
Chart: 
| Direct Mapped | 2-way | 4- way | Direct Mapped | 2-way | 4- way | Direct Mapped | 2-way | 4- way | Direct Mapped | 2-way | 4- way | Direct Mapped | 2-way | 4- way | Direct Mapped | 2-way | 4- way | mgrid | perl | su2cor | swim | tomcatv | turb3d
8 KB | 0.0886 | 0.0802 | 0.0707 | 0.0816 | 0.069 | 0.0652 | 0.0989 | 0.0819 | 0.073 | 0.0906 | 0.0822 | 0.0758 | 0.0726 | 0.063 | 0.059 | 0.0935 | 0.0608 | 0.0566
16 KB | 0.0694 | 0.0651 | 0.0624 | 0.063 | 0.0515 | 0.0488 | 0.0788 | 0.0666 | 0.0606 | 0.0756 | 0.0621 | 0.0602 | 0.0636 | 0.0584 | 0.0553 | 0.0508 | 0.0442 | 0.0407
32 KB | 0.0622 | 0.0602 | 0.0595 | 0.0455 | 0.039 | 0.0352 | 0.0605 | 0.0572 | 0.0562 | 0.0661 | 0.059 | 0.0569 | 0.0608 | 0.0533 | 0.0553 | 0.043 | 0.0358 | 0.0348
64 KB | 0.0601 | 0.0594 | 0.0586 | 0.0396 | 0.0326 | 0.0311 | 0.0563 | 0.0555 | 0.0552 | 0.059 | 0.0561 | 0.0556 | 0.0542 | 0.0531 | 0.0527 | 0.0354 | 0.0342 | 0.034

## Slide 9: Step 1: Results
Chart: 
| Direct Mapped | 2-way | 4- way | Direct Mapped | 2-way | 4- way | Direct Mapped | 2-way | 4- way | Direct Mapped | 2-way | 4- way | vortex | wave5 | ijpeg | li
8KB | 0.0875 | 0.0575 | 0.0981 | 0.0748 | 0.0657 | 0.0613 | 0.0327 | 0.0324 | 0.0291 | 0.0437 | 0.0261 | 0.0182
16KB | 0.0774 | 0.0615 | 0.0324 | 0.0585 | 0.0515 | 0.05 | 0.0293 | 0.024 | 0.0227 | 0.03 | 0.012 | 0.0109
32KB | 0.0596 | 0.047 | 0.0148 | 0.0532 | 0.048 | 0.0466 | 0.0251 | 0.0235 | 0.0217 | 0.026 | 0.0071 | 0.0064
64KB | 0.0265 | 0.0279 | 0.0141 | 0.0488 | 0.0472 | 0.0464 | 0.0219 | 0.0217 | 0.0217 | 0.0232 | 0.0052 | 0.0051

## Slide 10: Step 1: Analysis – Cache size
The cache size was varied by varying the number of cache lines for a fixed block size of 32Bytes.
We used the cache config command in Simplescalar for this purpose.
sim-cache -cache:il1 il1:512:32:4:f
Observation : As the cache size increases the miss rate decreases.

## Slide 11: Step 1: Analysis – Associativity
The benchmarks were run by varying the cache mapping policy.
The Associativity was varied by running the cache config command as follows:
sim-cache -cache:il1 il1:512:32:4:f
Observation: As the associativity increases the miss rate decreases.

## Slide 12: Step 1: Conclusion
Cache misses = Capacity misses + Conflict misses + Compulsory misses
As the cache size increases the capacity misses decreases. Hence the overall miss rate decreases.
As the associativity increases, the number of conflict misses decreases. Hence the overall miss rate decreases.

## Slide 13: Step 1 : Results
The miss rate is lowest for the biggest size of cache and associativity.
Best possible configuration : 64KB 4-way set associative cache.
Worst Performing Benchmarks: applu, fpppp, hydro2d, mgrid, su2cor, swim.

## Slide 14: Step 2: Varying Replacement policy
For 64KB, 4-way set associative configuration, we evaluated the replacement policy.
    LRU – Least recently used
    FIFO – First In First Out
    Random
Cache config command -cache:il1 il1:512:32:4:l/f/r

## Slide 15: Step 2: Results
Chart: IL1 Replacement without prefetch
| applu.ss | hydro2d.ss | fpppp.ss | mgrid.ss | su2cor | swim.ss
LRU | 0.0552 | 0.0387 | 0.0574 | 0.0586 | 0.0509 | 0.0517
FIFO | 0.0552 | 0.0387 | 0.0574 | 0.0586 | 0.0509 | 0.0516
RANDOM | 0.0583 | 0.041 | 0.0608 | 0.0612 | 0.0538 | 0.0546

## Slide 16: Step 2: Conclusion
LRU policy maintains the blocks which are most recently used in the cache.
FIFO policy maintains the blocks which are most recently added to the cache.
The benchmark programs seem to consists of a high percentage of “LOOPING”, in case of which the randomness in evicting an instruction/data from the cache may increase the misses, thus increasing the miss rate.

## Slide 17: Step 3: Performance Analysis
Worst benchmark program – mgrid.ss
Il1 miss rate = 0.0586
dl1 miss rate = 0.0918
il1 accesses = 15844
il1 replacements = 3
dl1 accesses = 7004
dl1 replacements = 0

## Slide 18: Step 3: Hypothesis for mgrid.ss
The number of il1 and dl1 replacements is only 3 and 0 i.e. the effect of conflict misses is very less.
Conflict misses have been optimized by using 4-way set associative.
Capacity misses have been reduced by increasing the cache size to 64KB.
Thus mgrid.ss is affected mainly due to “Compulsory misses”.

## Slide 19: GOAL
To implement an optimization technique to reduce compulsory misses.
PREFETCHING

## Slide 20: Optimization strategy: Prefetch Buffer
Compulsory misses occur due to the first time access to a block.
Increasing the block size decreases the compulsory misses, but not a way of optimization.
Logic behind optimization- Whenever a block is fetched from memory, if the next few sequential blocks are fetched and stored somewhere from which they could be accessed, then the number of compulsory misses decreases.
We implemented a Prefetch Buffer for this purpose.

## Slide 21: Prefetching strategy
L1 CACHE
PREFETCH BUFFER
MAIN MEMORY
PROCESSOR
L1 HIT
PREFETCH MISS: increment the misses.
Fetch a+1,a+2…
PREFETCH HIT: Prefetch the blocks
a+1, a+2…
Fetch block ‘a’
PREFETCH HIT:
For block ‘a’
L1 MISS: Look into Prefetch Buffer
PREFETCH MISS: Fetch ‘a’ in to Cache.

## Slide 22: Results after optimization
Chart: L1 Instruction Cache
| applu.ss | hydro2d.ss | fpppp.ss | mgrid.ss | su2cor.ss | swim.ss
Without prefetch buffer | 0.0552 | 0.0387 | 0.0574 | 0.0586 | 0.0509 | 0.0516
With Prefetch buffer | 0.0078 | 0.005 | 0.008 | 0.0073 | 0.0072 | 0.0069

## Slide 23: Results after optimization
Chart: L1 Data Cache Replacement Policy
| applu.ss | hydro2d.ss | fpppp.ss | mgrid.ss | su2cor.ss | swim.ss
Without prefetch buffer | 0.0797 | 0.0596 | 0.0914 | 0.0918 | 0.0755 | 0.0756
With Prefetch buffer | 0.0081 | 0.0056 | 0.009 | 0.0075 | 0.0084 | 0.006

## Slide 24: Percentage Improvement
Chart: L1 Instruction Cache Percentage improvement
| applu.ss | hydro2d.ss | fpppp.ss | mgrid.ss | su2cor.ss | swim.ss
Percentage improvement | 85.8696 | 87.0801 | 86.0627 | 87.5427 | 85.8546 | 86.6279

## Slide 25: Percentage Improvement
Chart: L1 Data Cache Percentage improvement
| applu.ss | hydro2d.ss | fpppp.ss | mgrid.ss | su2cor.ss | swim.ss
DL1 percentage improvement | 89.8369 | 90.604 | 90.1532 | 91.8301 | 88.8742 | 92.0635

## Slide 26: Conclusion
The miss rate was reduced by ~90% by implementing the prefetch buffer.
As the size of the prefetch buffer increases, more blocks are fetched from the main memory into the buffer. The miss rate decreases.
Prefetching accuracy = (hits/reads) increases as the buffer size increases.

## Slide 27: Future Scope
Multiple Prefetch buffers, miss rate could be further reduced.
Adaptive Prefetching.